## Slide 1
FINAL PROJECT
5G UE Context
Desynchronization
Detection & Recovery
A protocol-aware simulation for detecting persistent RAN–Core context mismatches and evaluating recovery.
TEAM
Laxminarayan Sahu 231IT035
Sandesh K 231IT061
Sujan H 231IT076
UE
RAN / gNB
CORE
KEY IDEA
Detect persistent disagreement between RAN and Core using fresh, aligned state observations.
Message fault
State divergence
Hidden condition
User impact
We measure detection before a failed consistency probe.
3
signaling procedures modeled
12
scenarios and controls
2,640
experiment runs
Notes: Scope: an abstract simulation, not a deployed 5G stack. Three procedures, 12 scenarios and 2,640 experiment runs. Team and design retained from original proposal.

## Slide 2
01 · INTRODUCTION
Where the UE context lives
RAN and Core each maintain a different part of the same user session.
U
UE
User device — phone, IoT, router. Requests access and services.
R
RAN / gNB
Radio connection, RRC state, radio bearers, mobility at the radio side.
C
AMF / SMF / UPF
Registration, mobility, PDU sessions, and the data path.
5G radio
N2 / control
1
RAN view
“Connected + bearer active”
↔
2
Core view
“PDU session active + QoS policy”
Both views describe the same UE — the network can keep running even when they quietly disagree.
Final Project • 5G UE Context Desynchronization Detection and Recovery
02
Notes: The Core aggregates responsibilities. N2 is control signaling; N3 is gNB-UPF user plane; N4 is SMF-UPF control. N4/UPF state is not separately simulated.

## Slide 3
02 · EXISTING WORK
What existing work provides
ICTC 2025 shows the value of AI-based anomaly detection on 5G Core KPI time series.
B
ICTC 2025 base paper
Cho et al., KT Corporation — AI-based large-scale time-series anomaly detection in 5G Core networks
Monitors time-series KPIs from Core network functions
Uses an Anomaly Transformer backbone
Point-Level Anomaly Amplification improves early sensitivity
Distribution-Aware Auto-Thresholding adapts score thresholds
Our comparison concerns scope; we do not reproduce its ML model
S
3GPP standards
TS 23.502 and TS 38.413 describe session and resource procedures. Our model abstracts them.
N
Simulation
Python / SimPy provides controlled, repeatable virtual-time experiments.
Final Project • 5G UE Context Desynchronization Detection and Recovery
03
Notes: Base paper: DOI 10.1109/ICTC66702.2025.11388910. Additional consistency work: DOI 10.1109/ICIN48450.2020.9059408. No ML baseline replication or general superiority claim.

## Slide 4
03 · LITERATURE GAP
From anomaly detection to state verification
KPI anomaly detection and per-UE protocol-state checking answer different questions.
E
ICTC 2025 approach
5G Core KPI time-series data
Statistical anomaly detection
Large-scale monitoring
Operator-network proof of concept
→
G
Identified gap
A KPI anomaly is not the same as a protocol-state inconsistency
Per-UE RAN–Core consistency is not the target
Does not necessarily show which state relationship is wrong
→
O
Our approach
Coupled context state models
Per-session semantic rules
Fresh, aligned observations
Pending-procedure awareness
Explainable alarms and recovery
Our contribution is an executable consistency-monitoring prototype. Worldwide novelty is not claimed.
Final Project • 5G UE Context Desynchronization Detection and Recovery
04
Notes: This is an engineering contribution under explicit assumptions. KPI anomaly detection and protocol-state contradiction detection use different inputs and definitions.

## Slide 5
04 · PROBLEM STATEMENT
The specific failure we target
A hidden RAN–Core state mismatch can persist until it becomes a service problem.
!
Problem
In 5G, UE context is maintained independently across the RAN and Core. Our problem is that after a signaling fault, the RAN and Core can hold different states for the same UE, and this hidden mismatch may remain undetected until it causes a service problem.
Faults represent application processing failures, not permanent SCTP packet loss.
R
RAN says
RRC_CONNECTED
QoS = new profile
C
Core says
PDU_SESSION_ACTIVE
QoS = old profile
MISMATCH = DESYNC
Final Project • 5G UE Context Desynchronization Detection and Recovery
05
Notes: The modeled RAN may apply a target before Core completion processing fails. NGAP reliable SCTP transport: TS 38.412, section 4.1. Application commit semantics here are experimental.

## Slide 6
05 · OBJECTIVES
What the project delivers
Implemented scope: session establishment, QoS modification and resource release.
01
Model
Coupled context state models
02
Verify
Orphan resources, access-resource mismatch and QoS mismatch
03
Simulate
Processing faults and delayed / reordered observations
04
Evaluate
Precision, recall, probe lead time and false alarms
05
Recover
Version-guarded context reconciliation
SCOPE
PDU session establishment
QoS modification
Resource release
Idle/resume and local cell change are controls. Full handover and N4 are outside the implemented scope.
Final Project • 5G UE Context Desynchronization Detection and Recovery
06
Notes: Formal model: research/formal_model.md. Release substitutes for the proposed full handover procedure; local cell change is a negative control. No RRC_INACTIVE implementation.

## Slide 7
06 · METHODOLOGY
How the prototype works
Implemented in Python and SimPy with separate node states, observations, labels and metrics.
1
Define FSMs
RAN states + Core states + coupling invariants
→
2
Generate traces
Timestamped snapshots per UE and session
→
3
Inject faults
Fail processing; delay or reorder observations
→
4
Run verifier
Align observations → check rules → raise alarm
→
5
Reconcile
Request context → align state → re-check
P
Prototype stack
Python · SimPy · snapshot adapter · rule-based verifier · Streamlit dashboard
Verified: 48 tests pass. Main benchmark: 1,920 runs. Held-out timing sensitivity: 720 runs.
Final Project • 5G UE Context Desynchronization Detection and Recovery
07
Notes: Core source: ue_context/model.py, simulation.py, verifier.py and metrics.py. Tests include the dashboard. Fault eligibility is per session with probability 0.7. The oracle uses actual state but shares semantic predicates.

## Slide 8
07 · CORE LOGIC
Detect first, then recover
Freshness, ordering and procedure guards separate accepted contradiction evidence from valid transitions.
R
RAN FSM
ABSENT
↕
APPLIED(q)
Access controls:
CONNECTED / IDLE
setup / modify / release
C
Core FSM
STABLE
↕
SETUP_PENDING
MODIFY_PENDING
RELEASE_PENDING
Committed record retained
!
Coupling rule example
RAN resources active + Core session absent: flag after valid observation guards and 12 ms persistence.
↻
Recovery hook
Query → refuse pending / changed versions → reconcile → verify (custom simulation adapter)
Final Project • 5G UE Context Desynchronization Detection and Recovery
08
Notes: Default timeout 110 ms, freshness 60 ms, grace 12 ms, polling 15 ms, monitor ticks 2 ms. Missing or temporally incompatible telemetry clears evidence. A timeout alone cannot prove permanent message loss. Recovery is bounded to two attempts.

## Slide 9
08 · EVALUATION
Measured evaluation results
40 paired seeds per scenario, six sessions per run. Values below refer to selected synthetic cases.
1
Precision / Recall: 1.00
QoS completion failure: 167 TP, 0 FP, 0 FN with aware detection.
2
Probe lead time: 18.35 ms
QoS completion failure, recovery off. Mean detection delay: 20.93 ms.
3
Delay false-positive rate: 0%
Aware: 0/240 sessions. Fixed 25 ms: 225/240 (93.75%).
4
Recovery: 167 / 167 jobs
QoS failed probes fall from 334 to 148 out of 720. Convergence is not connectivity.
SCENARIOS
Clean
Delay only
Processing loss
Reordering
High load
Truth comes from actual node states. Lead time uses consistency probes, not real call drops.
Final Project • 5G UE Context Desynchronization Detection and Recovery
09
Notes: Source: results/final-benchmark/summary.json. Each row aggregates 40 seeds. Lead time is conditional on a future failed probe in the same episode. Setup / release detection delays: 21.87 / 22.35 ms. Observation outage: 84.36 ms delay and no qualifying lead. Recovery under outage succeeds in only 15/167 jobs; unavailable adapter succeeds in 0/167.

## Slide 10
RESULTS · MEASURED EVIDENCE
False alarms under benign delay
False-positive sessions (%) among 240 sessions with no true desynchronization
Final Project • 5G UE Context Desynchronization Detection and Recovery
10
Chart: 
| Immediate | Fixed 25 ms | Protocol-aware
False-positive sessions (%) | 100 | 93.75 | 0
The fixed checker flags 225 of 240 sessions. The aware checker flags none.
Valid procedures remain within the 110 ms deadline. Delay alone is not a contradiction.
Notes: Source: results/final-benchmark/summary.json. 40 paired seeds, six sessions per run. Synthetic model; no real-network performance claim. Immediate 240/240 = 100%; fixed 225/240 = 93.75%; aware 0/240 = 0%. Each application leg is uniformly delayed 18–42 ms. No truth episodes occur in this scenario. Recall is undefined here.

## Slide 11
RESULTS · MEASURED EVIDENCE
Detection delay across fault scenarios
Mean virtual milliseconds after a true contradiction begins; aware detector, recovery off
Final Project • 5G UE Context Desynchronization Detection and Recovery
11
Chart: 
| Setup completion | QoS completion | Release completion | Queued high load | Observation outage
Mean detection delay (ms) | 21.87 | 20.93 | 22.35 | 22.48 | 84.36
Observation outages increase delay to 84.36 ms because fresh evidence is unavailable.
These are detection delays. They are not measured call-drop lead times.
Notes: Source: results/final-benchmark/summary.json. 40 paired seeds, six sessions per run. Synthetic model; no real-network performance claim. Delays: 21.87, 20.93, 22.35, 22.48, 84.36 ms. Conditional mean probe lead times: 138.15, 18.35, 22.67, 98.44, N/A. Probe timing is fixed and independent of alarms.

## Slide 12
RESULTS · MEASURED EVIDENCE
Recovery reduces failed consistency probes
Failed probes out of 720 per scenario; same seeds with recovery disabled and enabled
Final Project • 5G UE Context Desynchronization Detection and Recovery
12
Chart: 
| Setup | QoS | Release | High load | Observation outage | Adapter unavailable
Recovery off | 334 | 334 | 167 | 267 | 334 | 334
Recovery on | 0 | 148 | 41 | 21 | 334 | 334
QoS failed probes fall from 334 to 148, a 55.7% reduction.
Outages and adapter failure limit recovery. Passing a consistency probe does not prove connectivity.
Notes: Source: results/final-benchmark/summary.json. 40 paired seeds, six sessions per run. Synthetic model; no real-network performance claim. Failed off/on counts: setup 334/0, QoS 334/148, release 167/41, load 267/21, outage 334/334, adapter failure 334/334. Probes check actual stable context contradictions at 285,335,510 ms. Recovery success is distinct from probe success.

## Slide 13
RESULTS · MEASURED EVIDENCE
Detection accuracy and mismatch exposure
Aware detector without recovery; each row aggregates 40 runs
Final Project • 5G UE Context Desynchronization Detection and Recovery
13
Scenario | Detected | False alarms | Missed | Precision / Recall
Setup completion | 167 | 0 | 0 | 1.00 / 1.00
QoS completion | 167 | 0 | 0 | 1.00 / 1.00
Release completion | 167 | 0 | 0 | 1.00 / 1.00
Queued high load | 154 | 0 | 0 | 1.00 / 1.00
Observation outage | 167 | 0 | 0 | 1.00 / 1.00
QoS exposure with recovery: 15,698 → 6,192 session-ms (60.6% lower).
Perfect scores apply to these synthetic cases. They do not estimate operator-network accuracy.
Notes: Source: results/final-benchmark/summary.json. 40 paired seeds, six sessions per run. Synthetic model; no real-network performance claim. TP 167/167/167/154/167; FP and FN zero. Shared semantic predicates define both oracle and verifier rules, but the verifier never receives labels. Exposure is total episode duration over sessions, not elapsed time for one UE. Successful rollback may deactivate resources.

## Slide 14
09 · CONCLUSION
Conclusions and limitations
The scoped prototype detects modeled contradictions and reduces mismatch exposure with available recovery.
1
Problem
RAN and Core can hold different UE states after signaling faults.
2
Implemented solution
Coupled FSMs + protocol-aware consistency rules + controlled fault injection.
3
Measured benefit
QoS mismatch exposure falls from 15,698 to 6,192 session-ms across 40 seeds.
→
Next step
Validate on a RAN/Core testbed with user traffic, clock skew and full mobility. Current probes measure consistency only.
Final Project • 5G UE Context Desynchronization Detection and Recovery
14
Notes: Recovery reduces exposure in the chosen model. It can remove orphan resources without restoring a usable session. Six sessions per run do not establish scalability. Full handover, clock skew and packet delivery remain unvalidated.

## Slide 15
10 · REFERENCES
Key standards and supporting literature
Primary references for architecture, procedures, RRC, simulation, and anomaly monitoring.
[1]
3GPP TS 23.501
System architecture for the 5G System (5GS).
[2]
3GPP TS 23.502
Procedures for the 5G System (5GS).
[3]
3GPP TS 38.413
NG Application Protocol; resource setup, modification and release.
[4]
3GPP TS 38.412
NG signalling transport; reliable NGAP transfer over SCTP.
[5]
IEEE ICIN 2020
Sid-Otmane et al., Data Consistency in the 5G Specification (additional conceptual reference).
[6]
IEEE ICTC 2025
Y.-J. Cho et al., A Framework for AI-Based Large-Scale Time-Series Anomaly Detection in 5G Core Networks (base paper).
Source data: results/final-benchmark/summary.json. Procedure timings and recovery policy are experimental assumptions.
Final Project • 5G UE Context Desynchronization Detection and Recovery
15
Notes: https://doi.org/10.1109/ICTC66702.2025.11388910
https://doi.org/10.1109/ICIN48450.2020.9059408
https://www.etsi.org/deliver/etsi_ts/138400_138499/138412/16.00.00_60/ts_138412v160000p.pdf
Formal scope and measurement evidence are in the accompanying IEEE report.